Experiment Number 2

Objective: To study the characteristics of a single pump, two pumps in series and two pumps in parallel.

Equipment setup:

Basic equations and data:

Power output from a pump;

Overall efficiency of a pump;

| Speed | Input power, Pm, (Watts) | Motor speed (rpm) |
| --- | --- | --- |
| 1 | 40 | 750 |
| 2 | 70 | 1150 |
| 3 | 105 | 1850 |

1 bar = 100 kPa

Readings to be Taken:

## Table 1. Single pump

| No. | Volume(L) | Time(sec) | Q (L/sec) | (Pa) | (%) | Q2 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |

## Table 2. Pumps in series

| No. | Volume(L) | Time(sec) | Q (L/sec) | (Pa) | (%) | Q2 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |

## Table 3. Pumps in parallel

| No. | Volume(L) | Time(sec) | Q (L/sec) | (Pa) | (%) | Q2 |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |

Results:

We have,

Report the values of A and B for the three cases, i.e. single pump, pumps in series and parallel. These constants can be found by regression from vs.  for the three cases.

# Format for the report

The following sections must be included in the laboratory report

- Objective

- Equipment setup

- Theory

- Readings and calculations

# Graphs showing vs. for three cases, i.e. single pump, pumps in series and parallel on the same paper.

- Graphs showing and vs. for three cases on separate papers.

- Comments on the results

# Text boxes

C

Outlet

P1

B

P2

Inlet

A