# Design of Culverts

Typical cross-sections: Circular, arched, rectangular and oval

Flow Regimes:

## 1. Submerged-entrance condition

### Free-entrance conditions

Submerged entrance :

For Type 1

Total head loss = Head loss at entrance+ Friction loss + Head loss at exit

Neglecting the velocity head at 1 and 3

Hence the velocity can be computed as

and

This equation for velocity given above is valid for both Type 1 and Type 2 flows, which are sometimes called as the flows under outlet control.

In Type 3 the flow is similar to an orifice flow and hence

for square-edged entrance

for well-rounded entrance

In this situation (Type 3) the flow is under inlet control

In submerged entrance culverts the flow is more as compared to the unsubmerged entrance. But when it is not advisable to have submergence, we need to design unsubmerged entrance culvert.

### For Type 4 culvert

As may be seen the velocity of headwater is not neglected, because

Hence,

area at the critical flow section

### For Type 5

For Type 6

area at exit of the culvert

Determination of Flow Type in a culvert

Given: H, D, Tail water depth ye, Length of the culvert L, n and the type of entrance.

Submerged entrance:

- If , Type 1 flow, i.e.

- If , assume Type 2 flow and calculate Q by the respective equation and

- Calculate in the culvert. If , Type 2 flow is verified.

- If , calculate Q from the equation for Type 3 and calculate from it.

- If again, Type 3 is confirmed.

- If neither Type 2 nor Type 3 is verified, use the minimum of the two discharges as the capacity of the culvert.

Unsubmerged entrance:

- Assume Type 4 and Calculate . If  , Type 4 verified.

- Assume Type 5 and Calculate . If  , Type 5 verified.

- Assume Type 6 and Calculate . If  , Type 6 verified.

#### Design Considerations

Geometry of the culvert entrance is important. Four standard inlet types are:

- Flush setting in a vertical wall

- Wingwall entrance

- Projecting entrance

- Mitered entrance set flush with a sloping embankment.

Selection of the inlet configuration is based on:

  - Structural stability

  - Aesthetics

  - Erosion control.

USFHWA: US Federal HighWay Administration

Minimum Culvert size is specified by the local authorities (usually in the range of 30 to 60 cm).

Minimum Allowable Velocity: 0.6 to 0.9 m/s

Maximum Allowable Velocity: 3 to 4 m/s

Outlet protection should be provided for higher exit velocities.

Most common material used is concrete.

Example: What is the capacity of a 1.22m by 1.22m concrete box culvert (n=0.013) with a rounded entrance (ke=0.05, Cd=0.95) if the culvert slope is 0.5%, the length is 36.6m, and the headwater level is 1.83m above the culvert invert? Consider the following cases:

  - Free-outlet conditions, and

  - Tailwater elevation 0.304m above the top of the box at the outlet. What must the headwater elevation be in case (b) for the culvert to pass the flow that exists in case (a)?