# Design of Open Channels

## Basic Principles

Channel Flow

If depth of flow is unknown the above equation has to be solved by trials for most of the channel shapes.

# Newton’s Method to solve Manning’s equation

Error=		for Q=constant

Assuming n as constant

Now,

or

### Best Hydraulic Section

(1)

To minimize the cost of material used in the channel, we need to minimize the wetted perimeter, for given roughness, discharge and bed slope.

Consider a trapezoidal channel for example.

(2)

Eliminating the base width from above

(3)

Equating (1) and (3)

where, and Cn=1 for SI units.

Holding z constant and differentiating with respect to y and setting  we get,

(4)

Similarly holding y constant and differentiating with respect to z and setting , we get

Putting this value in (2), (3) and (4) we get the geometrical properties of the best trapezoidal section as

We can observe that  in this condition.

Similarly we can find the geometric characteristics of various shapes as shown in the following Table.

| Shape | Best Geometry | A | P | B |
| --- | --- | --- | --- | --- |
| Trapezoidal | Half hexagon |  |  |  |
| Rectangle | Half square |  |  |  |
| Triangle | Half square |  |  |  |
| Semicircle | - |  |  |  |
| Parabola | - |  |  |  |

### Minimum Permissible Velocity: 0.6 to 0.9 m/s

Channel Slopes :

Longitudinal Slope should be preferably equal to the ground slope, but if the permissible velocities are not achievable, the slope should be increased.

Side slopes depend on the type of the material, i.e. angle of repose.

USBR prefers a 1.5:1 (H:V) slope for usual sizes of lined channels.

Recommended side slopes are given in the Table below;

Freeboard: Vertical distance between the water surface and top of the channel.

Freeboard can be estimated as

Where, the coefficient,

The minimum freeboard is usually 30 cm.

At the channel bends additional freeboard must be provided to account for the super-elevation of the water surface. Super-elevation of the water surface can be estimated as

Where, average velocity in the channel, top width of the channel, and radius of curvature of the centerline of the channel.

It is also recommended that

## Lined Channel Design

According to ASCE all channels carrying supercritical flow should be lined with concrete reinforced in both longitudinal and lateral directions.

#### Steps in design

- Estimate the roughness coefficient, n for the lining material and freeboard coefficient, C for the design discharge.

- Compute the normal depth of flow by Manning’s equation, with assumed bed slope and if possible using best hydraulic cross-section.

- Check the minimum velocity and Froude Number. Repeat step 2 and 3 if necessary to meet the specifications.

- Calculate the required freeboard and increase the freeboard on the bends if required using the equation for super-elevation.

Example: Design a lined trapezoidal channel to carry 20 m3/s on a longitudinal slope of 0.0015. The lining of the channel is to be float-finished concrete. Consider: (a) the best hydraulic section, and (b) a section with side slopes of 1.5:1 (H:V).

Solution

- n=0.015,	for best section we compute,

# Text boxes

Bw

B=Bw+2zy

z

1

A

y

Free-board