Storm Water

Peak Runoff Models

Peak runoff is estimated only, not the full hydrograph

# Rational Method

where,

Runoff coefficient

Rainfall intensity

Catchment area

It is implicitly assumed that the excess rainfall rate =

Is runoff coefficient really constant???

For impervious areas C is constant.

Due to the assumed uniformity of the rainfall distribution, rational method is applicable to .

## Intensity-Duration-Frequency (IDF) Curve

Time of concentrationStorm duration, t

From kinematic wave equation;

## Minimum allowable

## Example 6.21

According to ASCE specifications, the rational formula should be used in two ways;

- Using the entire drainage area

- Using the most densely developed hydraulically connected area

Design discharge will be the highest from the above two approaches.

## Example 6.22

## Design of Storm Water Management Systems

## Major and Minor systems

## Storm sewers

Allowed to flow full. Check the energy grade line restriction according to the local regulations.

Cover: at least 0.9m

### Minimum allowable velocity: 0.6 to 0.9 m/s

Maximum allowable velocity: 3.0 to 4.0 m/s

## Example 6.37

## Example 6.38